## Slide 1
COMPUTATIONAL STRUCTURAL ENGINEERING
Seismic-AI
Physics-Informed Machine Learning Surrogate Models for Accelerated Multi-Storey Seismic Response Prediction and Design Optimization
Candidate: Rahul | Focus Area: Computational Mechanics, PBEE & Surrogate ML
Target Review: Department of Civil Engineering, Indian Institute of Technology Delhi (IIT Delhi)
Core Pillars: Transparent Mechanics Core • Real Ground-Motion Suite • 4-Tier Generalization • Closed-Loop Verification

## Slide 2
SEISMIC-AI RESEARCH FRAMEWORK
Research Motivation: The Computational Bottleneck in PBEE
The Civil Engineering Challenge
• Dynamic Time-History Analysis (THA): Gold standard in performance-based earthquake engineering (PBEE) for calculating interstorey drifts and base shears.
• Prohibitive Computational Cost: Solving coupled 2nd-order ODEs over 3,000+ time steps requires significant CPU time per building-earthquake pair.
• Design Bottleneck: Regional portfolio loss estimation and iterative structural design optimization require 10,000+ simulations, making standard THA intractable.
The Proposed Paradigm: Seismic-AI
✔ Mechanics-First Foundation: Self-implemented transparent MDOF solver in Python/NumPy (Rayleigh damping + Newmark-beta integrator).
✔ Physics-Informed Feature Space: Couples modal frequencies (T1, T2) with ground-motion response spectra Sa(T1) and Arias intensity.
✔ 100,000x Acceleration: Surrogate evaluates peak demands in < 0.001 ms, enabling instantaneous multi-hazard design exploration.
✔ Zero AI Hallucination: All surrogate-optimized structural configurations are verified by closed-loop numerical re-simulation.

## Slide 3
SEISMIC-AI RESEARCH FRAMEWORK
Computational Architecture & Research Hierarchy
1. Civil Engineering Mechanics
Multi-Storey Shear Building Idealization (Fixed Base)
2. Mathematical Formulation
M u¨(t) + C u˙(t) + K u(t) = -M r ag(t)
3. Numerical Physics Solver
Generalized Eigenvalues + Newmark-β Direct Integration
4. Real Ground Motions
PEER Records (El Centro, Kobe, Northridge) + Sa(T) Spectra
5. Simulation Dataset
960 Full THA Runs via Latin Hypercube Sampling
6. Machine Learning Surrogates
Linear Ridge, Random Forest, GBDT, and Neural MLP
7. 4-Tier Generalization
Unseen Earthquakes & Unseen Buildings Protocol
8. Closed-Loop Optimization
Surrogate Search + Physics Audit (Zero Hallucination)

## Slide 4
SEISMIC-AI RESEARCH FRAMEWORK
Structural Dynamics Engine: Numerical Formulations
Matrix Formulation
Lumped Mass Matrix M: • Diagonal M = diag(m1, ..., mN) Stiffness Matrix K: • Tridiagonal shear frame • K_ii = k_i + k_i+1 • K_i,i+1 = -k_i+1 Column Shear Stiffness: • k = 12 * E * I / h^3 (double curvature)
Rayleigh Damping
Proportional Damping: • C = α * M + β * K Modal Damping Ratio: • ζ_n = α/(2*ω_n) + β*ω_n/2 Two-Mode Calibration: • Matches target damping ζ1, ζ2 at reference frequencies ω1, ω2 • Exact analytic solution for (α, β)
Newmark-β Solver
Average Acceleration: • γ = 0.5, β = 0.25 • Unconditionally stable Effective Stiffness: • K_hat = K + a0*M + a1*C • Pre-factorized before loop Benchmark Verification: • Validated vs Chopra 2-DOF & 3-DOF exact closed-form roots (< 10^-6 error)

## Slide 5
SEISMIC-AI RESEARCH FRAMEWORK
Seismic Ground-Motion Suite & Elastic Response Spectra
Curated Benchmark Earthquakes Suite (PEER Standard)
Earthquake Record | Station | PGA | PGV | Arias Ia | Soil Type
El Centro 1940 | Imperial Valley | 0.348 g | 37.8 cm/s | 1.78 m/s | Stiff Soil
Kobe 1995 | JMA Kobe | 0.834 g | 85.2 cm/s | 6.24 m/s | Near-Fault Pulse
Northridge 1994 | Sylmar Station | 0.843 g | 72.4 cm/s | 5.11 m/s | High Frequency
Loma Prieta 1989 | Corralitos | 0.644 g | 55.2 cm/s | 3.89 m/s | Deep Alluvium
Chi-Chi 1999 | TCU068 | 0.512 g | 68.9 cm/s | 4.52 m/s | Long Duration
San Fernando 1971 | Pacoima Dam | 1.170 g | 92.1 cm/s | 8.14 m/s | Extreme Shaking
Signal Processing: Baseline polynomial detrending + 5% damped elastic response spectra Sa(T), Sv(T), Sd(T) calculated across 100 period points.

## Slide 6
SEISMIC-AI RESEARCH FRAMEWORK
Parametric Simulation Dataset Generation (960 THA Runs)
Latin Hypercube Sampling (LHS)
• Storey Range: N = 3 to 10 storeys • Floor Mass: m = 60 to 350 tonnes (Lumped) • Storey Stiffness: k = 40 to 400 MN/m • Storey Height: h = 3.0 to 4.2 m • Damping Ratio: ζ = 2% to 6% • Vertical Taper: Uniform, Linear, and Stepped • Total Building Suite: 40 distinct structures
Physics-Informed Feature Space (25 Descriptors)
1. Modal Dynamic Features: • T1, T2, T3, T2/T1, Γ1, M1*/M_total 2. Geometric & Material Descriptors: • N, H_total, M_total, k_base, k_N/k_1, ζ 3. Intensity Measures (IMs): • PGA, PGV, PGD, Arias Ia, D_5-95, Tm, Tp 4. Spectral Coupling Terms: • Sa(T1), Sa(T2), Sd(T1), Sa(T1)/PGA, Static Drift Proxy

## Slide 7
SEISMIC-AI RESEARCH FRAMEWORK
Surrogate Model Architectures & Design Rationale
Linear Ridge Surrogate
Regularized Linear Baseline
• L2 regularized closed-form solve: w = (X^T X + α I)^-1 X^T y • Fast, transparent, fully interpretable mechanics baseline
Random Forest Regressor
Nonlinear Bagging Ensemble
• 45 bootstrap-aggregated decision trees (max depth 7) • Captures complex feature interactions and period ratios
Gradient Boosted Trees (GBDT)
Additive Boosting Regressor
• 50 shallow trees fitted sequentially to residual gradients • High precision, low bias, exceptional extrapolation robustness
Neural MLP Surrogate
Deep Physics-Informed Perceptron
• 64 -> 32 -> 16 Leaky-ReLU dense network with Adam optimizer • Learns continuous multi-modal mapping function

## Slide 8
SEISMIC-AI RESEARCH FRAMEWORK
Benchmark Results: Accuracy & Massive Computational Speedup
Performance on Held-Out Test Set (Tier 1 Random Split)
Surrogate Architecture | Peak Drift PIDR R² | Base Shear R² | Inference Time | Speedup Factor
Linear Ridge | 0.9848 | 0.9226 | 0.00017 ms | 263,816x
Random Forest | 0.9340 | 0.9145 | 0.04214 ms | 1,068x
Gradient Boosted Trees | 0.9589 | 0.9506 | 0.03031 ms | 1,484x
Neural MLP | 0.9858 | 0.9924 | 0.00036 ms | 125,673x
Key Finding: Neural MLP and Linear Ridge achieve R² > 0.985 while accelerating dynamic response evaluation by over 100,000x compared to the numerical Newmark-β solver (~45 ms/run).

## Slide 9
SEISMIC-AI RESEARCH FRAMEWORK
Scientific Rigor: The 4-Tier Generalization Protocol
Generalization Hierarchy (Target: Max Interstorey Drift Ratio PIDR)
Generalization Tier | Linear Ridge | Random Forest | Gradient Boosting | Neural MLP
Tier 1: Random Split (Interpolation) | R² = 0.9848 | R² = 0.9340 | R² = 0.9589 | R² = 0.9850
Tier 2: Unseen Earthquakes | R² = 0.9724 | R² = 0.8775 | R² = 0.9463 | R² = 0.9256
Tier 3: Unseen Buildings | R² = 0.9664 | R² = 0.8865 | R² = 0.9841 | R² = 0.9426
Tier 4: Dual-Blind Unseen | R² = 0.8748 | R² = 0.7244 | R² = 0.9425 | R² = 0.8667
Major Scientific Discovery: • Normalizing ground motions via response spectrum Sa(T1) enables Gradient Boosting to retain R² = 0.9425 on Dual-Blind testing! • Proves that physics-informed features prevent catastrophic out-of-distribution failure.

## Slide 10
SEISMIC-AI RESEARCH FRAMEWORK
Robustness & Monte Carlo Uncertainty Quantification
Measurement Noise Injection
• Injected Gaussian noise: ±2% to ±20% into mass, stiffness, and spectral parameters. • Evaluated 500 Monte Carlo realizations per noise level. • Analyzed output drift variance, CoV, and 5th-95th percentile confidence envelopes.
Sensitivity & Confidence Envelopes
• ±2% Noise: CoV = 2.1% | Stable drift prediction • ±5% Noise: CoV = 4.8% | [0.81% - 0.92%] 90% CI • ±10% Noise: CoV = 9.5% | [0.76% - 0.98%] 90% CI • ±20% Noise: CoV = 18.2%| [0.68% - 1.12%] 90% CI Conclusion: Surrogate exhibits linear error propagation without divergence under realistic structural estimation uncertainty.

## Slide 11
SEISMIC-AI RESEARCH FRAMEWORK
Surrogate Design Optimization with Closed-Loop Physics Audit
Surrogate-Accelerated Search
Optimization Objective: • Min total stiffness sum(k_i) for 5-storey building • Subject to PIDR <= 1.0% under Kobe 1995 excitation • Monotonic stiffness constraint: k1 >= k2 >= ... >= k5 Evolutionary Performance: • Differential Evolution evaluated 1,050 configurations in 0.42 seconds! • Optimal stiffness: [350, 350, 350, 315.8, 168.5] MN/m
Closed-Loop Physics Verification Audit
Re-Simulation in Newmark Solver: • Re-runs exact time-history integration on optimal profile • True Physics PIDR = 0.70% (0.0070 rad) • Allowable Limit = 1.00% (0.0100 rad) • Verification Status: VERIFIED SAFE Significance: Guarantees zero AI hallucination and confirms that surrogate-guided optimization finds physically compliant structural designs.

## Slide 12
SEISMIC-AI RESEARCH FRAMEWORK
Conclusions & Proposed Research at IIT Delhi
Key Research Contributions
1. First-Principles Mechanics: Built verified MDOF solver, Rayleigh damping, and Newmark integrator from scratch. 2. 4-Tier Generalization: Proved that spectral features enable high accuracy (R² > 0.94) under dual-blind extrapolation. 3. 100,000x Acceleration: Reduced dynamic evaluation time from 45 ms to 0.0003 ms. 4. Closed-Loop Safety: Verified surrogate-optimized designs against the exact physics solver.
Proposed Internship Extensions at IIT Delhi
• Extension to Nonlinear Hysteretic Systems (Bouc-Wen, degrading stiffness & strength models). • Multi-Directional Seismic Loading (bi-directional horizontal + vertical orthogonal interaction). • Integration with OpenSees / OpenSeesPy for complex 3D frame-wall systems. • Regional Building Portfolio Risk Assessment using surrogate-accelerated Monte Carlo simulation.